## Slide 1: Bring Numerical Methods together
1
http://nm.MathForCollege.com
Transforming Numerical Methods Education for STEM Undergraduates

## Slide 2: Why Use Numerical Methods?

## Slide 3: Why Use Numerical Methods?
To solve problems that cannot be solved exactly

## Slide 4: Why Use Numerical Methods?
To solve problems that are intractable to solve exactly!

## Slide 5: Bascule Bridge THG

## Slide 6: Bascule Bridge THG
Trunnion
Hub
Girder
Notes: THG picture

## Slide 7: Trunnion-Hub-Girder Assembly Procedure
  Step1. Trunnion immersed in dry-ice/alcohol
  Step2. Trunnion warm-up in hub
  Step3. Trunnion-Hub immersed in dry-ice/alcohol
  Step4. Trunnion-Hub warm-up into girder

## Slide 8: Problem
After Cooling, the Trunnion Got Stuck in Hub

## Slide 9: Why did it get stuck?
Magnitude of contraction needed in the trunnion was 0.015˝ or more. Did it contract enough?

## Slide 10: What model should I use to calculate contraction of trunnion?

## Slide 11: Finding the fluid temperature to get enough contraction
Ta = 80oF
Tc = ???oF
D = 12.363"
∆D = -0.015"

## Slide 12: Finding the expression for thermal expansion coefficient

## Slide 13
What is the temperature of the trunnion after half an hour?

## Slide 14
How long does it take a trunnion to cool down?

## Slide 15
What is the rate of change of heat stored in the cylinder?

## Slide 16: Can you identify?
We talked about 7 mathematical procedures in this course. Write them down.
Now connect the problem just discussed to these 7 mathematical procedures on each of the previous slides.

## Slide 17: THE END