## Slide 1: Interpolation - Introduction
Reading Between the Lines

## Slide 2: What is Interpolation ?
Given (x0,y0), (x1,y1), …… (xn,yn), find the value of ‘y’ at a value of ‘x’ that is not given.
Figure Interpolation of discrete data.

## Slide 3
APPLIED PROBLEMS

## Slide 4: Fly Rocket Fly, Fly Rocket Fly
The upward velocity of a rocket is given as a function of time in table below. Find the velocity and acceleration at t=16 seconds.
0 | 0
10 | 227.04
15 | 362.78
20 | 517.35
22.5 | 602.97
30 | 901.67
Table Velocity as a function of time.
Velocity vs. time data for the rocket example

## Slide 5: Specific Heat of Carbon
A carbon block of mass 2kg is heated up from room temperature of 400K to 1500K. How much heat is required to do so?
Temperature (K) | Specific Heat (J/kg-K)
200 | 420
400 | 1070
600 | 1370
1000 | 1820
1500 | 2000
2000 | 2120

## Slide 6: Thermistor Calibration
Thermistors are based on change in resistance of a material with temperature. A manufacturer of thermistors makes the following observations on a thermistor. Determine the calibration curve for thermistor.
R (Ω) | T(°C)
1101.0 911.3 636.0 451.1 | 25.113 30.131 40.120 50.128

## Slide 7: Follow the Cam
A curve needs to be fit through the given points to fabricate the cam.
1
2
3
5
6
7
X
Y
4
Point | x (in.) | y (in.)
1 | 2.20 | 0.00
2 | 1.28 | 0.88
3 | 0.66 | 1.14
4 | 0.00 | 1.20
5 | –0.60 | 1.04
6 | –1.04 | 0.60
7 | –1.20 | 0.00

## Slide 8
END

## Slide 9: Length of a Path

## Slide 11
END

## Slide 12: Spline Method of Interpolation http://nm.MathForCollege.com

## Slide 13: Why Splines ?

## Slide 14: Why Splines ?
Figure : Higher order polynomial interpolation is a bad idea

## Slide 15: Linear Spline Interpolation

## Slide 16: Linear Spline Interpolation (contd)

## Slide 17: Example
The upward velocity of a rocket is given as a function of time in Table 1. Find the velocity at t=16 seconds using linear splines.
Table Velocity as a
function of time
Figure. Velocity vs. time data
for the rocket example
(s) | (m/s)
0 | 0
10 | 227.04
15 | 362.78
20 | 517.35
22.5 | 602.97
30 | 901.67

## Slide 18: Linear Spline Interpolation

## Slide 19: Quadratic Spline Interpolation

## Slide 20: Quadratic Spline Interpolation (contd)

## Slide 21: Quadratic Spline Interpolation (contd)

## Slide 22: Quadratic Spline Interpolation (contd)

## Slide 23: Quadratic Spline Interpolation (contd)

## Slide 24: Quadratic Spline Example
The upward velocity of a rocket is given as a function of time. Using quadratic splines
Find the velocity at t=16 seconds
Find the acceleration at t=16 seconds
Find the distance covered between t=11 and t=16 seconds
t | v(t)
s | m/s
0 | 0
10 | 227.04
15 | 362.78
20 | 517.35
22.5 | 602.97
30 | 901.67

## Slide 25: Data and Plot
t | v(t)
s | m/s
0 | 0
10 | 227.04
15 | 362.78
20 | 517.35
22.5 | 602.97
30 | 901.67
Notes: 25

## Slide 26: Solution
Let us set up the equations

## Slide 27: Each Spline Goes Through Two Consecutive Data Points

## Slide 28
t | v(t)
s | m/s
0 | 0
10 | 227.04
15 | 362.78
20 | 517.35
22.5 | 602.97
30 | 901.67
Each Spline Goes Through Two Consecutive Data Points

## Slide 29: Derivatives are Continuous at Interior Data Points

## Slide 30
Derivatives are continuous at Interior Data Points
At t=10
At t=15
At t=20
At t=22.5

## Slide 31: Last Equation

## Slide 32: Final Set of Equations

## Slide 33: Coefficients of Spline
i | ai | bi | ci
1 | -0.15667 | 24.271 | 0
2 | 1.2021 | -2.9053 | 135.88
3 | -0.44893 | 46.627 | -235.61
4 | 2.2315 | -60.589 | 836.55
5 | 0 | 39.827 | -293.13

## Slide 34: Final Solution

## Slide 35: Velocity at a Particular Point
a) Velocity at t=16
235.61

## Slide 36
Acceleration from Velocity Profile
b) Acceleration at t=16

## Slide 37: Acceleration from Velocity Profile
The quadratic spline valid at t=16 is given by
,

## Slide 38: Distance from Velocity Profile
c) Find the distance covered by the rocket from t=11s to t=16s.
Notes: 38

## Slide 39: Distance from Velocity Profile

## Slide 40
END
http://nm.MathForCollege.com

## Slide 41: Points for Robot Path
x | y
2.00 | 7.2
4.5 | 7.1
5.25 | 6.0
7.81 | 5.0
9.20 | 3.5
10.60 | 5.0
Find the shortest but smooth path through consecutive data points

## Slide 42: Polynomial Interpolant Path

## Slide 43: Spline Interpolant Path

## Slide 44: Compare Spline & Polynomial Interpolant Path
Length of path
Polynomial Interpolant=14.9
Spline Interpolant =12.9